## Slide 1: SDN Architecture issue 1.1 Introduction
Dave Hood
May 2016

## Slide 2: Status
Architecture issue 1 TR-502 published June 2014
Architecture issue 1.1 TR-521 published February 2016

## Slide 3: Why an architecture?
Learning how to think about the problem is 80% of the solution
Multiple perspectives are okay, in fact better than okay, but …
Different but compatible perspectives
Incompatible perspectives
Integrated view

## Slide 4: One-slide summary, Architecture issue 1
SDN controller B
(Physical) data plane
Manager B
Customer G application
Controller plane
(Virtual) data plane
(Virtual) data plane
Customer R application
SDN controller G
(Physical) data plane
Manager G
SDN controller R
(Physical) data plane
Manager R
Controller plane
Controller plane
(Virtual) data plane

## Slide 5: Since issue 1: hot topics
Intent NBI
  Specify (only) the desired outcome and constraints
  Tell me what you want, not how to do it!
Agile new services
  Flexibility for services not even imagined today
East-west interface
Enterprise SDN
Relation to ETSI NFV
Multiple protocols between the same pair of entities: OpenFlow-switch, NETCONF/OF-config, SNMP, OVSDB …

## Slide 6: Why SDN ?
To deliver services to customers (aka users, aka clients, aka apps)
  … in an optimum way
Issue 1.1 focuses on services
  Services are invoked downward through a process of orchestration
  Until they meet resources exposed upward through a process of virtualization (issue 1)
  Service and resource views are complementary

## Slide 7: Clients
Client is usually a separate business entity
  Security, information hiding, policy enforcement
  Interface can be (semi-)transparent depending on circumstances
Client may be a complex organization (e.g., enterprise)
  Client-server association includes business agreement and policies
  Within an association: Multiple services, multiple users, multiple host platforms

## Slide 8: Clients
Client requests services in its own terms
  The only resources in client request may be the client’s point(s) of attachment
  and even these may be implicit (attachment point of the device I’m using right now)
  Client expects server (aka SDN controller) to orchestrate additional resources as needed
Server (SDN controller) may not understand client’s terms
  “Bob is (or is not) allowed to connect to the Internet.”
  A mapping is required (possibly transparent)
  Developing a non-transparent mapping is necessarily a joint responsibility
It is often beneficial to minimize the client’s view of underlying resources
Simpler client
Simpler mapping
Security – reduced attack surface
More freedom for SDN controller to satisfy client requirements

## Slide 9: Takeaway: client contexts
A client context is the conceptual container on a server (SDN controller) that represents everything needed to support a particular client
  Security credentials, stack parameters
  Exposed virtual and supporting resources
  Hidden resources
  Client-specific mappings
  Custom code
  Services (later slide)
  Provider’s policy for this client
    Response to illegal client requests, e.g. deny, flag for human decision, accept but charge extra
    Interpretation of legitimate client activity, e.g. how to achieve traffic isolation
If client business relationship terminates, delete client context, reclaim resources
Much of client context is persistent
  Backup/restoration – may contain client-confidential information
  Some parts may pertain to more than one SDN controller, e.g. to support roaming

## Slide 10: Background: Management-control continuum
If there is human involvement, we tend to call it management.
If it’s fully automated, we call it control.
MCC recognizes a continuum between these extremes.
The device being managed-controlled neither knows nor cares.
Control is intelligence in a feedback loop.
  Defines the essence of an SDN controller
The sine qua non of an SDN controller

## Slide 11: Services
Vertical lines on SDN pictures are management-control relationships
  What about the data plane?
A service usually involves data-plane exchanges between client and server (and possibly other) domains
A service always exists in some client context
A service usually continues to operate even without a current management- control session
Introduce concept of service context
  Contained in client context
  Contains persistent information about each currently active service
  If service terminates, delete service context and reclaim resources
  Decouples service from possible different logins of the given client organization

## Slide 12: Service delivery … in an optimum way
Map client request to SDN controller (server)
SDN controller responsible to orchestrate resources and services within its direct control, along with others in other domains if needed
Orchestration is
    the continuing
      optimization
        of available resources and services
          in light of client demand
            according to some optimization policy.
Orchestration is inextricably bound up with virtualization
Dynamic feedback control is a key feature of SDN orchestration
Multi-dimensional real-time optimization is the real value of an SDN controller
  Complex problem, will lend itself to a range of implementation options

## Slide 13: Putting it all together
SDN controller is at the core of the architecture
All interfaces are the same
  Service invocation, service delivery
  Resource exposure, resource consumption
Only the roles differ
  Scope, privilege, policy

## Slide 14: East-west SDN controllers

## Slide 15: Enterprise user

## Slide 16: Summary: Hot topics (1)
Intent NBI
Client context, service context, joint responsibility for mapping
Agile new services
Requires only development of mapping onto standard interface
Standard interface may expand over time
As a standard, the interface can safely be used by 3d party developers, customers, providers, etc.
Common semantics most important, ties into ONF information modeling project
Relation to ETSI NFV
Well-known that SDN can provide connectivity to NFV
Can also provide real-time optimized connectivity to NFV
But SDN also acts as the consumer of VNF and NS resources
Ties into ONF TR-518
East-west interface
SDN controllers may peer by acting as clients and servers to each other.

## Slide 17: Summary: Hot topics (2)
Open source
Architecture provides uniform view to understand how things fit together
Facilitates gap analysis and suitability for purpose
OF-switch, OF-config, SNMP, OVSDB …
Client context with multiple parallel sessions, separate view and privilege for each
Enterprise SDN
Client context, client administrator, multiple logins, multiple services

## Slide 18: To-do list
Market the architecture
  Develop architecture overview and/or handout material
  Develop white papers to illustrate applicability to various cases
    E.g. UNIFY, BBF, 5G
Collect errors, omissions, needs, opportunities
  May lead to corrigendum or eventually an issue 1.2

## Slide 19
Questions?